## Slide 1
Stage 2 Interview
Sports Biomechanics Data Scientist Task
Thomas Aston

## Slide 2
Data selection:
Requirements
Low cost
Portable/
non-invasive
Stride
sensitive

## Slide 3
Foot
contact
Foot
flat
Foot
off
Foot
contact
Foot
flat
Foot
off
Foot
contact
Foot
flat
Foot
off
Data selection:
Events

## Slide 4
Data selection:
Open data

## Slide 5
Foot strike and foot off
Speed invariant
Real time
Event detection:
Requirements

## Slide 6
Event detection:
Implementation
FOR each new sample (left_gyro_y, right_gyro_y, timestamp):
FOR each foot ∈ [left, right]:
# 1. Real-time smoothing
smoothed = mean(last 15 gyro_y samples)
# 2. Detect MSW (zero-crossing + local min)
IF (prev_smoothed ≥ 0 AND smoothed < 0):
state = AFTER_ZERO_CROSSING
IF state = AFTER_ZERO_CROSSING:
IF is_local_min(smoothed_history) AND smoothed < msw_threshold:
EMIT MSW(timestamp)
# 3. Detect other events (prev_msw exists)
stride_time = Δt(MSW)
IF stride_time ∈ [0.1, 2.5] s:
seg = smoothed[prev_msw : curr_msw]
MS = argmin(seg[30–60%]); EMIT MS
FS = argmax(seg[start : MS]); EMIT FS
FO = argmax(seg[MS : end]); EMIT FO
prev_msw = curr_msw
state = SEARCHING
Handles new samples as they ‘arrive’
Analyses both feet
Causal filtering
State machine: check for zero-crossing
Detect local minima (mid swings)
Check for valid, complete stride (pair of mid swings)
Detect mid stance (min. velocity norm)
Update state machine
Detect foot strike and foot off (maxima)

## Slide 7
Event detection:
Performance

## Slide 8
Event detection:
Performance

## Slide 9
Event detection:
Performance

## Slide 10
Metrics:

## Slide 11
Demo:
movetru-stride.streamlit.app

## Slide 12
Validation:
Lab
Goal:
Event timing accuracy + agreement of key metrics.
Reference:
Force plates (vertical GRF)
Pressure insoles (total force/ROI)
Mocap (kinematic proxy)
Protocol:
n≈20
varied speeds, conditions
1-2 min/condition
dual-foot IMUs
synced start
Scoring:
Detection: Precision/Recall/F1 score (match within threshold)
Timing: Bias and Limits of Agreement (Bland-Altman)
Derived metrics: stride, stance, swing etc.

## Slide 13
Validation:
Field
Goal:
Real-world robustness & timing accuracy across terrains/speeds relevant to sport.
Reference:
Pressure insoles (total force / ROIs)
High-speed video 120–240 fps (spot checks)
(Optional) foot pod for cadence cross-check
Sync: clap/stomp; slate visible in video
Protocol:
Diff. surfaces and movements (relevant to sport)
Walk -> sprint; include fatigue
≥1000 strides total; dual-foot IMUs; natural footwear
Stress test: sensor alignment, sweat/rain, different shoes
Scoring:
Detection: Precision/Recall/F1 score (match within threshold)
Timing: Bias and Limits of Agreement (Bland-Altman)
Derived metrics: stride, stance, swing etc.